## Slide 1: Agricultural-water use (AG) Package for gsflow
Hyper-resolution modeling of Regional water use by agriculture with integrated hydrology

## Slide 2: Agricultural-water use (AG) Package for gsflow
Developed using concept of Net Irrigation Water Requirement (NIWR)
How much water should be diverted/pumped to provide well-watered conditions?
How does water supply limit consumption?
+

## Slide 3: Agricultural-water use—at the intersection of supply and demand
Demand estimated using land use, climate, and ET deficit
Hydrology model simulates water supply
Competition among different water sectors (ag., muni, res., indus.)
Energy Demand
Water Supply

## Slide 4: Energy and Soil-Water balance used to estimate NIWR
,
ETww is the well-watered ET (e.g., Penman-Monteith)
Actual ET (ETa) and irrigation is subject to water supply, irrigation schedule, and other constraints
--Irrigation processes happen automatically in GSFLOW/MODFLOW
Inverse problem: determine SW+GW irrigation amounts by minimizing the ET deficit:
GSFLOW

## Slide 5: Irrigation option 1 (simple)
Irrigation demands (NIWR) are specified as time series SW diversions or GW pumping rates
Water supply limits irrigation and GW can be used to automatically supplement SW
ET can be simulated in fields or efficiency factors can be specified to remove crop consumption from model
Return flows can be simulated
ETww/ETa

## Slide 6: solution for NIWR-option 2
Actual ET (ETa) is a nonlinear function of NIWR, apply Newton method:
Chart: Applied irrigation, cfs
| 0 | 2.5 | 9.9724998469999999 | 10.84809589 | 14.04295254 | 14.50526619 | 14.55909729
 | 1 | 4 | 9.1951 | 9.3682 | 9.9201 | 9.9917 | 9.9999
Chart: Applied irrigation, cfs
| 0 | 2.5 | 9.9724998469999999 | 10.84809589 | 14.04295254 | 14.50526619 | 14.55909729
 | 1 | 4 | 9.1951 | 9.3682 | 9.9201 | 9.9917 | 9.9999
i=2
i=3
i=4
i=7
Q
ETww/ETa
Demand
Energy/water budget
Irrigate farms
GSFLOW
SW+GW

## Slide 7: solution for NIWR-option 3
Irrigation is “triggered” by field conditions:
Energy/water budget
Calculate
Divert SW, pump GW
Irrigation continues while:
Irrigation rate specified by user and can be supplemented by groundwater
Irrigate fields

## Slide 8: Example problem 1
MODFLOW-ONLY
Energy and water budget calculated by UZF Package
3,440 acres of irrigated fields

## Slide 9: Imposed irrigation schedule (maximum SW diversions)
Irrigation is constrained to periods of non-zero flow shown by green line

## Slide 10: Conjunctive-USE of Surface water and groundwater
Dry climate
SW diversions
Moderate climate
GW Pumping
More supplementary groundwater pumping for dry climate

## Slide 11: Impacts of field soil texture on NIWR (groundwater only)
Coarse soils require more irrigation due to rapid percolation below root zone

## Slide 12: Example problem 2
GSFLOW
ENERGY AND SOIL-WATER BALANCE CALCULATED BY PRMS
27.5 hectares of irrigated fields

## Slide 13: impacts of crop type (crop coefficient)

## Slide 14: Irrigation amounts determined by minimizing ET deficit
Surface water and groundwater irrigation amounts for low and high crop coefficient (Kc) values
High precipitation
Low annual irrigation
Low precipitation
High annual irrigation

## Slide 15: Comparison of niwr for 2 options (Trigger verses demand)
Average annual NIWR=1.4 meters
Average annual NIWR=0.9 meters

## Slide 16: Differences in irrigation for options

## Slide 17: AG Package for gsflow
Automatically distributes water for irrigation using energy/water budget and mimics different types of grower behavior
Internal demand calculation for GSFLOW, considers evolving water supply conditions
Climate change impacts on agriculture, low flows, groundwater levels, and reservoirs available through GSFLOW

## Slide 18: AG Package Input file structure (Key words)
Well list can use TABFILES to change max constraint on pumping